## Slide 1
Peter Munk Cardiac Centre · AI Team
Text and Box Prompted
3D Medical Segmentation
Architecture · Optimization · Measurement · Deployment
Brian Xiao · VoxTell and nnInteractive · Fir cluster, Alliance Canada

## Slide 2
What This Covers
02
Part | Content | Slides
1. Context | The task, and two ways of prompting a segmentation model | 3 to 5
2. Architecture | How VoxTell and nnInteractive are actually built | 6 to 17
3. Optimization | Four changes, what each one bought | 18 to 24
4. Measurement | Four artifacts that inflated the result, and the fixes | 25 to 32
5. Results | Speed and accuracy, with the caveats attached | 33 to 39
6. Deployment | Skills, MCP and plugins, and the validation gate | 40 to 46
7. Limits | Where the models fail, and what is still open | 47 to 51
The measurement section is the part I would most want questions on.

## Slide 3
The Task
03
Given a 3D scan, outline a structure.
Input is a volume: a CT or MR study, typically 200 to 900 slices
Output is a binary mask, one voxel label per position
Scored with Dice Similarity Coefficient: overlap with expert annotation, 0 to 1
Manual annotation of one organ across a volume takes a trained reader tens of minutes
Why it is hard in 3D
A 512 x 512 x 400 volume is 105 million voxels. It does not fit in GPU memory as one
forward pass, so the volume is tiled into overlapping patches and stitched back together.
That tiling is where most of the inference time goes, and where most of the speedups live.
DSC above roughly 0.7 is generally considered clinically usable. Lesions score well below organs for every model in this class.

## Slide 4
Two Ways to Say What You Want
04
Text prompt
segment("the spleen")
Any structure the language model can name
No interaction needed, so it batches
Requires a language model in the loop
Accepts any string, including nonsense
Spatial prompt
segment(bbox=[[z0,z1],
[y0,y1],
[x0,x1]])
The box defines the target, so no vocabulary limit
Cheap: no text encoder at all
Needs a human to place the box
Cannot be wrong about what you meant
The tradeoff drives everything downstream: cost, failure modes, and what can be automated.

## Slide 5
The Two Models
05
 | VoxTell v1.1 | nnInteractive v1.0
Prompt | Free text | Point, scribble, box, lasso
Origin | DKFZ, CVPR 2026 submission | DKFZ, CVPR 2025 challenge baseline
Backbone | Residual Encoder U-Net | Residual Encoder U-Net (ResEnc-L)
Patch size | 192 x 192 x 192 | 192 x 192 x 192
Extra cost | Qwen3-Embedding-4B text encoder | None
Training scale | Not published in the checkpoint | 64,518 volumes, 717,148 objects
Same backbone family, same patch size, completely different front end.
VoxTell rows read from models/voxtell_v1.1/plans.json. nnInteractive rows from arXiv 2503.08373 and this project's own runs.

## Slide 6
PART 2
Architecture

## Slide 7
VoxTell: Inference Pipeline
07
Preprocess
crop to non-zero, z-score
→
Text encode
Qwen3-Embedding-4B
→
Sliding window
192 cubed patches
→
Postprocess
sigmoid, insert crop
Where the time went, before optimization
Phase | Time | Share
Preprocessing | 0.09s | 2.8%
Text embedding | 2.17s | 67.3%
Sliding window | 0.94s | 29.2%
Postprocessing | 0.02s | 0.6%
Text embedding dominated, so caching it was the first target
Sliding window is the floor: it is the actual segmentation
Preprocessing and postprocessing are noise at this volume size
RTX 4070 SUPER, 1 prompt, warm model, no cache. OPTIMIZATION_REPORT_COMPACT.md section 2.

## Slide 8
VoxTell: Segmentation Backbone
08
dynamic_network_architectures.architectures.unet.ResidualEncoderUNet
Stage | Channels | Blocks | Stride | Resolution
0 | 32 | 1 | 1, 1, 1 | 192 cubed
1 | 64 | 3 | 2, 2, 2 | 96 cubed
2 | 128 | 4 | 2, 2, 2 | 48 cubed
3 | 256 | 6 | 2, 2, 2 | 24 cubed
4 | 320 | 6 | 2, 2, 2 | 12 cubed
5 | 320 | 6 | 2, 2, 2 | 6 cubed
Six stages, 32x total downsampling
Residual blocks weighted to the deep stages, where context matters
Conv3d with InstanceNorm3d and LeakyReLU
Decoder is light: one conv per stage, transposed conv upsampling
Deep supervision off at inference
Read from models/voxtell_v1.1/plans.json, configurations.3d_fullres.architecture.arch_kwargs.

## Slide 9
VoxTell: The Text Side
09
Prompt string
"the spleen"
→
Qwen3-Embedding-4B
4B parameter encoder
→
Embedding
2560 dimensions
→
Query
2048 dimensions
The projection
self.project_text_embed = nn.Sequential(
nn.Linear(text_embedding_dim, 2048),
nn.GELU(),
nn.Linear(2048, query_dim), # query_dim = 2048
)
A 4B parameter language model runs before any segmentation starts
That is the entire reason text prompting is expensive
It is also fully cacheable: the same prompt always gives the same vector
This observation is optimization 2
Projection from voxtell/model/voxtell_model.py. Embedding width from OPTIMIZATION_REPORT_COMPACT.md section 1.

## Slide 10
VoxTell: How Text Becomes a Mask
10
A MaskFormer style head. The text embedding is used as a query, not as a class label.
Text query
2048-d, from the prompt
→
Transformer decoder
6 layers, 8 heads, pre-norm
→
Per-stage projection
2048 to channels x 32 heads
→
Dot with features
mask logits per scale
The decoder attends over image features at stage 4 (320 channels, 12 cubed), with a 3D positional encoding
The refined query is projected separately for each of 5 mask-former stages
A dot product between query and decoder feature map gives the mask at that scale
So the prompt does not select from a fixed label set. It parameterises the mask directly, which is why the vocabulary is open
Dimensions read from the checkpoint, not from constructor defaults, which disagree: project_text_embed is (2048, 2560), pos_embed is 1728 = 12 cubed, and the stage-4 projection is 10240 = 320 x 32 heads.

## Slide 11
VoxTell: Prompt Decoder Internals
11
Parameter | Value | Note
d_model | 2048 | query dimension throughout
Layers | 6 | TRANSFORMER_NUM_LAYERS
Heads | 8 | TRANSFORMER_NUM_HEADS
Feedforward | 2048 | inner width of each layer
Norm placement | Pre-norm | normalize_before=True
Positional encoding | 3D sinusoidal | flattened over h, w, d
Attention | Self then cross | query attends to image features
Each layer
self_attn (query to query)
multihead_attn (query to image)
linear1 -> GELU -> linear2
three LayerNorms, residual adds
Standard transformer decoder, used for prompt fusion rather than generation
Cheap next to the 4B text encoder: it runs on a single 2048-d query token
voxtell/model/transformer.py, with every width confirmed against fold_0/checkpoint_final.pth rather than the constructor defaults.

## Slide 12
VoxTell: One Design Choice That Matters Later
12
"data_identifier": "nnUNetResEncUNetLPlans_noResampling_3d_fullres"
VoxTell v1.1 does not resample to a target spacing.
Most nnU-Net configurations resample every scan to a fixed voxel size first
This one does not, and the inference path has no resampling step either
So the network sees voxels at whatever spacing the scan was acquired at
Through a fixed 192 cubed patch, that changes the physical field of view
Acquired spacing | What one patch covers
1.0 mm | 192 mm of anatomy
5.0 mm | 960 mm, longer than a torso
This turns into a measured accuracy
falloff on slide 48.
plans.json, configurations.3d_fullres.data_identifier. Confirmed by grep over voxtell/inference/predictor.py: no resampling call.

## Slide 13
nnInteractive: Inference Pipeline
13
Set image
volume, no text
→
Add interaction
box, point, scribble, lasso
→
AutoZoom
expand ROI until captured
→
Refine
sliding window at full res
No text encoder, so cost per prompt starts far lower than VoxTell
Interactive by design: the model expects to be corrected and re-run
The session holds the image, so repeated prompts on one volume are cheap
The checkpoint must be loaded with fold='all'. Using fold 0 scores about 0.33 DSC and is not a valid baseline
API from nnInteractive v1.0. The fold='all' requirement was found the hard way on this project and is documented in the plugin skill.

## Slide 14
nnInteractive: Early Prompting
14
Prompts are not a separate branch. They are extra input channels.
Channel group | Count | Carries
Image | 1 | the scan itself
Point | 2 | positive and negative clicks
Scribble | 2 | positive and negative strokes
Lasso and box | 2 | the two share one pair
Previous prediction | 1 | the model's own last output
The network is a U-Net over a stack of channels, not an encoder plus a prompt module
Feeding the previous prediction back is what makes refinement iterative
A correction is just another channel edit and another forward pass
Backbone is the nnU-Net Residual Encoder L configuration, the same family as VoxTell
arXiv 2503.08373, early prompting. The paper describes the channel groups; the exact total is not quoted here because the paper does not state it in one place.

## Slide 15
nnInteractive: AutoZoom
15
The model decides its own field of view.
Predict in ROI
start tight around the prompt
→
Check borders
does the mask touch the edge?
→
Zoom out 1.5x
repeat, up to 4x total
→
Resize and refine
sliding window at full res
Small objects never pay for a whole-volume pass
Large objects still get captured, because the ROI grows until the mask stops touching the border
The cost is data dependent, which makes per object timing noisier than VoxTell's
do_autozoom=True is the default and was left on for every measurement here
arXiv 2503.08373: ROI expands by a factor of 1.5 iteratively, up to 4x zoom out, then the low resolution mask is resized and refined with a sliding window.

## Slide 16
nnInteractive: Training Scale
16
120+
public 3D datasets
64,518
volumes
717,148
annotated objects
Spans CT, MR, PET, ultrasound and microscopy
That breadth is the reason a bounding box generalises to structures it was never given a name for
It is also why the vocabulary question does not arise: there is no label set to be outside of
VoxTell trades that for the ability to be asked in words, which is a different kind of generality
arXiv 2503.08373. Figures are the paper's, not measured here.

## Slide 17
Architectures Side by Side
17
 | VoxTell v1.1 | nnInteractive v1.0
Backbone | ResidualEncoderUNet, 6 stages | nnU-Net ResEnc-L
Channels | 32, 64, 128, 256, 320, 320 | Same family
Patch | 192 cubed | 192 cubed
Prompt enters | As a transformer query, late | As input channels, early
Prompt encoder | Qwen3-Embedding-4B, 4B params | None
Head | MaskFormer style, 5 scales | Standard segmentation head
Resampling | None | Not stated in the paper
Iterative | No | Yes, previous prediction fed back
Late fusion buys an open vocabulary. Early fusion buys iteration and a much cheaper prompt.

## Slide 18
PART 3
Optimization

## Slide 19
What I Was Trying to Do
19
Minimise end to end GPU inference latency without losing accuracy.
Accuracy is the constraint, not the objective. A faster model that segments worse is not a result
So every speed change is paired with a DSC measurement on the same checkpoint
Target hardware is the H100 MIG 3g.40gb partition on Fir, with an RTX 4070 SUPER for local iteration
Both models were already accurate. The question was only whether they could be made cheaper
Constraint that shaped everything
Inference only. No retraining, no fine tuning, no architecture changes. The checkpoint is
fixed, so any accuracy change is a bug in what I did rather than a property of the model.

## Slide 20
Optimization 1: Sliding Window Overlap
20
tile_step_size 0.5 to 0.75
Patches overlap so that stitching artifacts do not appear at patch boundaries
At step 0.5 each patch overlaps its neighbour by half, which is generous
At 0.75 the overlap drops and the patch count falls with it
Combined with cropping to the non-zero bounding box, 25 patches became 9 on the test case
0.94s to 0.82s
sliding window, 1 prompt, RTX 4070 SUPER
+0.0003
DSC, so no accuracy cost
13% reduction on this phase. The DSC figure is the full 5 case AMOS evaluation, not the single timing case.

## Slide 21
Optimization 2: Two Level Embedding Cache
21
The same prompt always produces the same vector. There is no reason to compute it twice.
In memory
LRU dict, about 5 KB per entry
On disk
SHA-256 keyed .pt files
Miss
run Qwen3 and store
2.17s to under 0.001s
in memory cache hit
Lookup is a dict get plus a GPU memory copy
Disk layer survives across sessions: 0.02s on NVMe, 0.04s on Lustre
This is the single largest win, because embedding was 67% of runtime
It matters clinically: the same anatomical queries repeat across every volume in a study
Cache state is asserted empty before every cold measurement. A warm cache on one arm and a cold cache on the other was one of the four artifacts.

## Slide 22
Optimization 3: INT4 Text Backbone
22
bitsandbytes NF4, double quantized, FP16 compute
BitsAndBytesConfig(
load_in_4bit=True,
bnb_4bit_quant_type='nf4',
bnb_4bit_use_double_quant=True,
bnb_4bit_compute_dtype=torch.float16,
)
8 GB to 2 GB
text backbone VRAM
NF4 is designed for normally distributed weights, which transformer weights approximately are
Double quantization compresses the quantization constants too, worth about 0.4 bits
The point is fitting on a 12 GB card, not speed
The failure mode worth knowing
_load_text_backbone builds the config inside a try block and catches every exception, falling
back to FP16. If bitsandbytes or accelerate is missing, the model loads, reports INT4 in the log,
and runs FP16. Nothing downstream would tell you. The plugin checks for this separately.
voxtell/inference/predictor.py, _load_text_backbone. Both packages were undeclared dependencies until this project added them.

## Slide 23
Optimization 4: Numba Preprocessing
23
@numba.njit(parallel=True) over crop to non-zero and z-score normalisation
Replaces the NumPy implementation with a compiled, parallel one
Compiles once per process, then runs at native speed
Result: no measurable gain
0.09s before, 0.09s after on the RTX. 0.14s both ways on the cluster CPU. On the first call it is
actually slower, because that call pays the JIT compile. Preprocessing is under 3% of runtime, so
there was never much to win here.
Reported because a negative result is still a result. Optimising a 3% phase was the wrong place to spend effort, and measuring it is how that became visible.
The one place it may still pay is multi-prompt or much larger volumes, which has not been tested.

## Slide 24
Things That Did Not Work
24
Approach | Outcome | Why
ONNX plus ORT CUDA | 14x slower than PyTorch | ORT lacks cuDNN 3D convolution kernel support
torch.compile on VoxTell | 1.00x, no change | Triton unavailable on Windows; model is compute bound
Numba preprocessing | No measurable gain | Phase is under 3% of total runtime
Batched sliding window | Built, not yet paid off | batch_size=1 today; needs H100 80 GB to matter
torch.compile did work on nnInteractive, at 1.33x. Same technique, different model, opposite result. That is worth more than either number alone.
VoxTell is bound by 3D convolution throughput, which compilation does not change
nnInteractive makes many small calls per object, where dispatch overhead is the cost

## Slide 25
PART 4
Measurement

## Slide 26
The First Number I Reported Was Wrong
26
VoxTell speedup, as measurement error was removed
26x
baseline ran on CPU
17.6x
no warm-up, cache mismatch
7.1x
first arm ate start-up cost
2.7x
measured correctly
Not one of those corrections changed the code being measured.
The optimizations always did exactly what they do. Every drop came from the benchmark flattering them. A 10x error in the reported result, entirely in the measurement.
The next four slides are each one of those errors.
The largest error surfaced by running the same script on two GPUs and noticing that phases which should behave the same did not.

## Slide 27
Artifact 1: The Baseline Ran on CPU
27
26x
reported
What actually happened
The baseline loaded the text encoder in FP32
FP32 Qwen3-4B needs about 16 GB; the card has 12 GB
The allocation failed and the model fell back to CPU
So a GPU run was being compared against a CPU run
Why it was not obvious
Nothing errored. The run completed, produced a correct mask, and returned a plausible time.
The only signal was that the baseline was slower than it had any right to be, and that only
looks wrong if you have an expectation of how fast it should be.
Fix: assert the device of every module before timing, and hold precision identical across arms.

## Slide 28
Artifact 2: Cache State Differed Between Arms
28
17.6x
reported
What actually happened
The optimized arm ran second, after the baseline had populated the cache
So it read the embedding from memory while the baseline computed it
That is a real 2000x gain on that phase, but it is the cache, not the algorithm
Reporting it as one number conflates two different claims
The fix is to report both, separately.
Claim | Number | What it measures
Algorithmic | 1.8x cold | tile_step and Numba, both arms cold
Full stack | 2.0x warm | the same plus a cache hit
fair_benchmark_results.txt, RTX 4070 SUPER, abdominal CT. Cache is now asserted empty before every cold arm.

## Slide 29
Artifact 3: Whichever Arm Ran First Paid Start-Up
29
7.1x
reported
What actually happened
CUDA context creation, cuDNN algorithm selection and kernel autotuning all happen on first use
The baseline always ran first, so it absorbed all of it
On the H100 this alone moved the result from 1.0x to 7.1x
The fix, and a bug it caused
Warm the GPU, the text backbone and the sliding window path before timing anything. The first
attempt warmed with a 4x4x4 dummy volume, which crashed InstanceNorm3d: a single spatial
element has no variance to normalise over. The warm-up has to run at the real patch size, 192
cubed, or it is not warming the kernels that actually run.
Expected more than 1 spatial element. This is why warm-up code has to be as carefully written as the thing it is warming.

## Slide 30
Artifact 4: Precision Was Not Held Constant
30
If one arm runs INT4 and the other runs FP16, quantization is being counted as an algorithmic gain.
INT4 is a legitimate optimization, but it is a different claim from tile_step or caching
Mixing them means the headline number cannot be attributed to anything in particular
Both arms in the final benchmark run INT4, so what is left is algorithmic only
The INT4 gain is then measured separately, against its own baseline
The general rule this produced
Change one thing per comparison. If two things differ between arms, the result is a fact about
the pair and cannot be attributed to either. This sounds obvious written down and was violated
three separate ways before it was written down.

## Slide 31
The Rules That Came Out of It
31
Hold precision constant, so quantization cannot pose as algorithmic gain
Warm the GPU, the text backbone and the sliding window path before timing
Assert the embedding cache is empty before every cold measurement
Assert the device of every module, rather than assuming the flag took effect
Repeat to n >= 4 and quote the range, never a single run
Compare an effect against run to run spread before calling it real
Never compare across GPUs without saying so
Every one of these exists because it was violated first. They are written into a preflight script that refuses to submit a job that breaks them.

## Slide 32
Turning Rules Into a Preflight Check
32
python validate_job.py my_benchmark.sh
[ ok ] venv matches model voxtell env
[ ok ] HF_HOME exported
[ ok ] allocation rrg-jma
[ ok ] gpu slice MIG
[ FAIL ] warmup present whichever arm runs first absorbs
CUDA init; this inflated 1.0x to 7.1x
[ FAIL ] cuda sync before timer timings measure kernel launch only
BLOCKED: 2 checks failed. Fix these before submitting.
Eleven checks, each one traceable to a job that already failed or a number that was already wrong
Deliberately textual and simple: a validator nobody can read is a validator nobody runs
Catches allocation, CPU over-request, MIG slice, unbuffered output and log paths as well
voxtell-plugin/skills/voxtell-inference/scripts/validate_job.py. It also refuses shell variables in SBATCH directives, which SLURM does not expand.

## Slide 33
PART 5
Results

## Slide 34
VoxTell: Speed
34
Change | Effect | DSC
Sliding window | tile_step 0.75 plus crop to non-zero, 25 to 9 patches | +0.0003
Embedding cache | repeat prompts return a stored tensor | identical
INT4 backbone | 8 GB to 2 GB VRAM, enables the 12 GB card | 0.97 agreement
Numba preprocess | no measurable gain at this volume size | unchanged
2.7x mean
abdominal CT, H100 MIG · 2.6 to 2.8x across 4 runs
One run: 3.27s to 1.28s
Case CT_AMOS_amos_0018 (63x512x512). Both arms run INT4, so precision is held constant and this is algorithmic gain only.

## Slide 35
VoxTell: Accuracy
35
+0.0003
tile_step 0.5 to 0.75 · 0.8090 to 0.8093
65 objects across 5 abdominal CT cases
Measured against expert annotation
Same checkpoint on both arms
13 abdominal organs, AMOS, seed 42
No pass/fail threshold applied
One caveat, stated plainly
INT4 quantization is on by default
0.97 agreement with full precision
Segments 5.5% fewer voxels
One sided, so bias rather than noise
Measured on one case, not the full set
VoxTell DSC from accuracy_results.csv. The INT4 comparison is n=1 and measures output agreement, not accuracy against ground truth.

## Slide 36
An Accuracy Bug Worth Showing
36
The same volume, the same prompt, the same checkpoint.
0.2978
read with nib.load().get_fdata()
0.9864
read with NibabelIOWithReorient
VoxTell was trained through a reader that reorients the volume to a canonical axis order
Reading it any other way leaves the array in its stored orientation
The model then segments a plausible looking fragment of the wrong thing
It does not error. The only way to catch it is to score against ground truth
This is the same shape of failure as the CPU baseline: a wrong answer that looks like a right one.
Found while building the plugin, by scoring a demo run against ground truth rather than eyeballing the mask.

## Slide 37
nnInteractive: Compiling the Network
37
torch.compile(session.network, mode='reduce-overhead')
One line changed
Fuses kernels and cuts per-call dispatch overhead
1.33x
per object, mean of 4 runs
Range 1.28 to 1.39x, so a 33% gain against an 8% spread
One job: 0.288s to 0.215s per object, which is 1.34x on its own
+0.0002
mean DSC change · 294 objects
No run showed degradation
Speed and accuracy from the same jobs
CPU time held at 6:18 to 6:33 across runs while walltime fell, which is what a GPU bound workload looks like.
20 CT cases from the CVPR validation set, fold='all' checkpoint, H100 MIG 3g.40gb. CPU efficiency 13 to 20% of the 8 cores requested.

## Slide 38
The Speedup Is Not Free at the Start
38
Compiling costs time before the first prediction.
23.6s
one-time compile
0.071s
saved per object
~22 cases
to break even
Batch of 881 validation cases: clearly worth it
Radiologist with 3 scans: never recovered
A batch optimization, and it should not be sold as anything else
23.6s measured on node-local /tmp. The shared filesystem is slower, so treat it as a lower bound. About 331 objects at 14.7 objects per case.

## Slide 39
Results Summary
39
 | Speedup | Accuracy | Evidence
VoxTell | 2.7x (2.6 to 2.8x) | +0.0003 DSC | 4 speed runs, 65 objects for DSC
nnInteractive | 1.33x (1.28 to 1.39x) | +0.0002 DSC | 4 runs, 294 objects
Still Open
Speedup measured on a single CT volume
INT4 under-segments 5.5%, on one case only
Batched sliding window built but not yet paid off
Next
Repeat across more CT volumes and prompt types
Run INT4 against all 881 validation cases
TensorRT FP16 engine on Fir
The most useful thing I built was a benchmark that kept catching itself.

## Slide 40
PART 6
Deployment

## Slide 41
A Model That Cannot Say No
41
VoxTell is text prompted, so it accepts any string.
Send an abdominal CT and ask for a brain tumour
It runs. It returns a mask. The mask is of nothing
Nothing in the pipeline says so, so you get a plausible result and no warning
This is the same failure shape as the CPU baseline and the orientation bug
The question Dr. Ma posed
Skills define workflow, protocol, when to use something and how to run it. Default VoxTell may
still run a brain tumour prompt on an abdomen CT. A skill can help generate the answer that the
model cannot segment a brain tumour from an abdominal CT.

## Slide 42
Skills, MCP Servers and Plugins
42
Mechanism | What it is | What it can do
Skill | Instructions loaded into the model's context | Shapes how the model works: workflow, protocol, standards. Advisory
MCP server | A process exposing callable tools over JSON-RPC | Real code with real return values. Deterministic. It can refuse
Plugin | A package bundling skills, MCP servers, commands and hooks | One installable unit, versioned and distributable
The distinction that matters
A skill can tell the model that a brain prompt on an abdominal CT is wrong.
Only a tool can make the call fail.
One is guidance the model may or may not follow. The other is a gate it cannot walk past.

## Slide 43
The Validation Gate
43
Request: REFUSED
The prompt asks for a structure in the brain (brain, brain tumor), but the
image is a CT study of the torso. That structure is not in this field of
view, so any mask returned would be meaningless.
Image
modality : CT
region : torso
shape : (406, 512, 512) spacing: (1.25, 0.82, 0.82)
- intensities reach -2048, consistent with Hounsfield units (air ~ -1000)
- 25.0% of voxels below -700 HU (air)
- 508 mm of coverage spans thorax and abdomen together
Returns an error, not a mask. No model is loaded and no GPU is touched
The refusal states what it inferred and why, so a wrong refusal is visible rather than mysterious
Real output from the installed plugin on a FLARE abdominal CT with the prompt 'brain tumor'.

## Slide 44
How the Gate Decides
44
Intensity statistics and geometry, not a classifier. A validator nobody can audit is a validator nobody should trust.
Signal | Rule | Why
Modality | CT is calibrated in Hounsfield units, so air sits near -1000 | MR intensities are arbitrary and rarely negative
Region | Air fraction plus field of view | A head has almost no internal air; a torso has lungs or bowel gas
Prompt | Anatomy vocabulary mapping terms to regions | Deliberately incomplete: an unknown term never blocks
Refuses only on a clear mismatch. Unknown on either side proceeds with a note
Adjacent regions pass, since thorax and abdomen routinely share a field of view
A validator that blocks whatever it cannot classify is useless
voxtell-plugin/mcp_server/validate.py. Thresholds are stated in the source and printed in every response.

## Slide 45
What the Plugin Exposes
45
Tool | Purpose
check_request | Validate an image and prompt pair. No compute. Returns modality, region and the reasoning
voxtell_segment | Text prompted segmentation. Validates first, refuses on mismatch unless forced
nninteractive_segment | Bounding box prompted segmentation, with box validation ahead of the GPU check
list_models | What is available and what each model can and cannot do
setup | Check the machine, report which build is live, fetch the checkpoint
Written against the MCP wire protocol directly, with no SDK dependency, so the protocol stays readable
Two transports from the same routing code: stdio for Claude Code, streamable HTTP for hosted clients
Installs in two commands from a GitHub marketplace, on Windows and on Ubuntu
github.com/pentaexe/VoxTell-main. Verified end to end on Windows and on a clean Ubuntu machine by a second tester.

## Slide 46
What Packaging It Exposed
46
Building an installer found bugs that running it locally never would.
Bug | Symptom | Why it hid
numba undeclared | Clean install could not import the predictor at all | My machine had numba from something else
bitsandbytes undeclared | INT4 silently served FP16 | The loader catches every exception
5D array to the session | nninteractive_segment had never once run | It had never been exercised
print() to stdout | Corrupted the JSON-RPC stream | One client tolerated it
Same name and version as PyPI | pip could not tell fork from stock | Both reported voxtell 0.1.0
Every one of these is the same pattern as the benchmark artifacts: it worked, it looked right, and it was wrong.

## Slide 47
PART 7
Limits and Next Steps

## Slide 48
Where VoxTell Falls Off
48
Five MSD-Liver cases, prompt 'liver tumor'. Mean DSC 0.720, median 0.861.
The gap disappears once you sort by slice thickness.
Case | z-spacing | Slices | DSC
MSD-Liver_000 | 5.0 mm | 75 | 0.479
MSD-Liver_001 | 5.0 mm | 123 | 0.520
MSD-Liver_003 | 1.0 mm | 534 | 0.861
MSD-Liver_004 | 0.8 mm | 841 | 0.868
MSD-Liver_002 | 1.0 mm | 517 | 0.872
Both failures are the thick slice scans. Nothing overlaps
The mechanism is slide 12: no resampling, fixed 192 cubed patch
At 5 mm that patch spans 960 mm of anatomy
A 15 mm lesion is 15 slices at 1 mm and 3 at 5 mm, so the boundary is smeared
Out of distribution acquisition geometry, not a model defect
Independent run by a second tester on our Fir dataset. n=5, and nothing in the sample sits between 1 mm and 5 mm.

## Slide 49
Turning That Into a Warning
49
Caveat
Coarsest voxel spacing is 5.0 mm. VoxTell v1.1 does not resample, so
accuracy falls off on thick-slice scans: measured DSC 0.48 and 0.52 on two
5 mm liver-tumour cases against 0.86-0.87 on three at 0.8-1.0 mm (n=5).
Where the falloff begins between 1 mm and 5 mm has not been measured.
Expect a usable mask on a large target and an unreliable one on a small lesion.
Fires at 3 mm or coarser, before any GPU time is spent
A caveat and not a refusal: the request is legitimate and the mask is still useful on a large target
The point is that it is said before a DSC is written down, rather than after
3 mm is conservative, not measured. The deck and the code both say so
Same shape as the anatomy gate, applied to acquisition geometry instead.

## Slide 50
Limitations, Stated Plainly
50
VoxTell speedup is measured on a single CT volume, n=4 runs. It is not a distribution
The INT4 agreement figure is n=1 and measures output agreement, not accuracy against ground truth
The slice thickness finding is n=5 with a plausible mechanism, which makes it a strong hypothesis rather than a result
DSC scales with target size. The five liver cases ranged over 543x in ground truth volume, so their mean is not a clean summary
The region heuristic is thresholds on one CT convention, and is untested on MR beyond the modality check
nnInteractive numbers come from the CVPR validation set only
The HTTP transport has no authentication and must not be exposed without an auth layer in front
Every number in this deck has a source line. If a figure has no provenance, it should not be here.

## Slide 51
What I Would Take From This
51
Both models got faster without losing accuracy: 2.7x and 1.33x, each with a DSC measurement attached
The reported speedup fell by 10x under scrutiny, and not one correction changed the code
The same failure shape kept recurring: a run that completes, looks right, and is wrong
CPU baseline, cache mismatch, warm-up ordering, reader orientation, silent FP16 fallback, a 5D array
So the durable output is not the speedup. It is the checks that make those visible
A preflight validator, a regression suite that synthesises its own data, a build provenance check,
and two gates that refuse work before it is wasted. Those outlast any particular number.